## Slide 1: ＊Power Source with no loss in load current
＊Capacitor Input circuit generates about 10% of load current loss, twice in every cycle.
Notes: コンデンサ・インプット回路はコンデンサの電位が基準になり、Di側の電位が低いときは、コンデンサの電位が電位差となり、Ωの法則道理、負荷電流が流れます、Di側の電位が上昇コンデンサと同電位になると、電位差のないループ回路はΩの法則道理、負荷電流が流れません、Di側電位がコンデンサの電位より上昇すると電位差が生じ電流が流れだしますが、放電後のコンデンサは並列に入っている負荷よりインピーダンスが低いので整流電流はさきにコンデンサに流れ込むため、この間約半サイクルの10％が負荷電流欠落を起こしています。

## Slide 2: ＊Critical Defect in Capacitor input Circuit
＊There exists time-zone for the current not flowing despite showing voltage on the
waveform in voltmeter and oscilloscope.
＊There exists time-zone for the current not flowing despite showing voltage on the
waveform in voltmeter and oscilloscope.

## Slide 3: ＊In Ohm’s Law, I=V/R This V shows a potential difference.
＊The waveform in oscilloscope does not distinguish Electrical Potential from Potential Difference, displaying together.
●When a potential on Di side is lower than capacitor potential, capacitor potential is Potential Difference（V) in every way.（Ｂ→Ｃ）●When Potential on Di side rises ,with Potential becoming the same potential, there is no potential difference (V) in closed circuit, with no flow of current.（Ｃ point）
●Red Waveform Waveform displayed in oscilloscope
●The reality (Red Waveform) is that the waveform which extracts Voltage (Potential Difference) only.
●When load current is cut off, rectifying circuit becomes the cause of noise generation.
When red part is connected to voltage V(potential difference) only according to Ohm’s Law, you will get Ｉ＝V／R, potential difference (voltage) as shown in Ohm’s Law. If you take a look at voltage waveform, at the time of switching over, you will understand that the current does not flow at 0 V of potential difference.
Fig.1ーCapacitor Input Rectifying Circuit and Voltage & Current Waveform
Notes: コンデンサ・インプット回路はコンデンサの電圧が基準になり、Dｉ側電位がコンデンサ電位より高くなると、電位差が生じ,DIが整流を開始しコンデンサの充電と負荷電流供給を行います、問題は測定器が、電位と電位差の区別ができず、表示してしまいます、Ωの法則のI=V/RのVは電位差をさします、また、ダイオード電流が流れても放電後のインピーダンスの低いコンデンサに先に電流が流れ込むためダイオード電流３ｍｓのうち１／３がコンデンサに流れ込み、負荷電流欠落をおこしています。

## Slide 4: Second Generation Series Power Source＋CPM
＊The second generation power source compensates for 10% of loss current.
＊The noise generated in rectifying circuit dis-appears..
Result
＊The 10% of music signal lost by load current loss can be reproduced (gets closer to original sound.） If noise disappears, it gets closer to the sound of natural world
(reproduced sound of music signal only).
CPM
＊Loss signal at the time of generating reverse voltage is reproduced.
Notes: 第2世代電源は放電後の低インピーダンスのメインCに突入する整流電流の補填のため、別整流回路に倍の容量のCを用意しておき、メインCの充電と負荷電流の供給することで、負荷電流欠落をカバーします。

## Slide 5: Second Generation Series Power Source Circuit and Rectifying Waveform
CRT1
CRT2
C0 is main capacitor, and C1 shows volume Capacitor (2 times of CO) in the other rectifying circuit.
Notes: CRT2は従来の整流回路のダイオード電流波形、CRT2は別整流回路に倍の容量のCから流れ出す、メインコンデンサC0の補填電流と負荷が必要とする負荷電流。

## Slide 6: Fourier Analysis which is generated due to load current loss
Capacitor Input Circuit
Second Generation Capacitor Input Circuit
Noise level 200mV ＠１A, which basic waveform and noise level are buried at 400Hz.
Clearly separate Basic Waveform from Noise Level up to 1200Hz and with Noise Level at 1mA@1A
Notes: When flowing 1A, Load current loss in conventional rectifying circuit is 200mV at 50Hz. Basic waveform gets equal to noise level at 400Hz. Power source noise is amplified together with voice signal. Meanwhile, fourth generation, which has no load current loss, shows 1mA of noise level and basic waveform is clearly expanded to 1200Hz. AMP Power Source makes it possible to amplify voice signal only.

## Slide 7: Result
●Conventional power source generates 10% of load current loss twice in every two cycles.
As we listen to voice signal, blended with noise which generates music signal loss in power source circuit, we are forced to listen to the sound different from that of natural world.
●Human’s eyes and ears are unable to make judgment, since brain revises to look at and listen. (It might be said of the difference between Berlin Phil-Harmonia Orchestra and NHK Symphony Orchestra?)
However, if you make comparative audition, you can judge it in one audition.
●In second generation series power source, you can listen to the sound closer to natural world, as you listen to noise-free, 100% music signal only.
●CPM function is to help reproduce more real voice by correcting weakness of direct current circuit.